## Slide 1: Computational Electromagnetics & Remote Sensing
Uday Khankhoje,
Electrical Engineering, IIT Madras uday@ee.iitm.ac.in

## Slide 2: The Roadmap
Microwave remote sensing and the Synthetic Aperture Radar (SAR)
Why we care? Context of upcoming NASA-ISRO mission: NISAR
Electromagnetic and signal processing framework for SAR
Examples
  soil moisture detection
  vegetation analysis
  deformation studies of Earth’s surface

## Slide 3: Remote Sensing: Various types
Optical, Infrared: e.g. Google satellite view photos, Hubble space telescope
Microwave: estimation of soil moisture, ocean wind speed etc, creating digital elevation maps.
Active: Satellite is source of illumination
Passive: Some other source (usually the sun)

## Slide 4
Microwave remote sensing offers all-weather capability

## Slide 5: Making it specific …
We will focus on active microwave remote sensing in the remainder of this tutorial.
Change radar wavelength => we can access different parts of the Earth’s surface

## Slide 6: Why is this important?
NASA-ISRO joint mission, NISAR will be launched in 2020.
NISAR tech specs:
  L & S band radars (first time ever dual band)
  Fully polarimetric : 165 Watts / pol
  12 day repeat orbit
  3-10m resolution
  750 km orbit height

## Slide 7: Why is this important?
Huge amounts of data will be generated, on a global scale
Big opportunity to study:
  Earth surface: Surface deformation to determine the likelihood of earthquakes, volcanic eruptions, and landslides, and monitor groundwater, hydrocarbon, and sequestered CO2 reservoirs
  Cryosphere: determine how climate and ice masses interrelate and raise sea level and measure changes in sea ice, snow extent, permafrost, and surface melting.
  Ecosystems: determine the contribution of Earth's biomass to the global carbon budget and characterize ecosystem disturbance and impacts on biodiversity.
  Water: determine aquifer extent and change over the Earth's vulnerable water systems.
Indian academia is quite unprepared to meet the challenge

## Slide 8: Nomenclature and geometry

## Slide 9: Range Resolution

## Slide 10: Range resolution

## Slide 11: Range resolution
Putting it together, the ground resolution becomes
Approximating pulse band-width as gives the ground resolution as
Small implies lower SNR, but poorer range resolution

## Slide 12: Range Resolution
Instead use a longer pulse, but modulate it, e.g. a chirp. Net result: SNR is good, and B also high.
Now, the echoes from two targets may overlap in time, but they get returned at different frequencies
=> Frequency filtering helps to recover resolution
Matched filter: convolve return signal with a replica of transmitted signal:
Resolution depends on B, not pulse length
Typically: ~tens of s, B ~tens of MHz

## Slide 13: What about azimuth resolution?

## Slide 14: Real aperture radar

## Slide 15: Solution: Synthetic Aperture Radar

## Slide 16: SAR – utilizing Doppler
If is the range at any point, then received signal is (ignoring other factors)
Due to satellite motion, say velocity , changes as
Since , we have

## Slide 17: SAR – utilizing Doppler
Inst. frequency is
Total time object is in beam?
Bandwidth is
Using a matched filter, signal duration of processed pulse:

## Slide 18: SAR – utilizing Doppler
Two points separated along azimuth by:
Min separation s.t. they can be resolved:
Remarkable result: Resolution independent of wavelength!
But, no free lunch as small length also => poor SNR

## Slide 19: SAR processing challenges
Inadequate pulse repetition frequency (PRF) can cause aliasing of the image, seen above.

## Slide 20: SAR imaging artifacts

## Slide 21: SAR images: speckle
Average the scene over many “looks” to reduce speckle noise.
Leads to some loss of resolution

## Slide 22: SAR Polarimetry

## Slide 23: SAR Polarimetry

## Slide 24: Power of SAR polarimetry

## Slide 25: End of introduction

## Slide 26: Major classes of scatterers
Bare, rough soils
Crop covered soils
Forests (different kinds)
Urban areas
Water bodies
In each of the above cases, for each object is different, and hence radar scatter changes.

## Slide 27: Important example: soil moisture
Role in water cycle; input parameter to climate models
[Vadose Zone Modeling with VADOSE/W; Krahn 2004, Geo-Slope.]

## Slide 28: Important example: soil moisture
Important for crop yield prediction; especially for places with scarce availability of water
For places with excess rainfall; important for flood prediction and disaster management

## Slide 29: Soil Moisture Missions
Aircraft based mission in progress (AirMOSS) P-band
Satellite based mission launched in 2014 (SMAP) L-band
NASA-ISRO mission (NISAR) L&S band – 2020 launch

## Slide 30: Analyzing bare rough soils
Complication: statistic of soil surface also influence radar backscatter,
For e.g. surface roughness, or correlation length have a strong impact on

## Slide 31: In real life …
[http://soils.cals.uidaho.edu/ soilorders/orders.htm]
Soil can be heterogeneous in:
Composition,
Moisture content, especially after rainfall/irrigation
Soil Physics; Marshall et. al., Cambridge UP, 1996.

## Slide 32: In real life …
[http://soils.cals.uidaho.edu/ soilorders/orders.htm]
Soil can be heterogeneous in:
Composition,
Moisture content, especially after rainfall/irrigation
Analytical and semi-analytical methods fail to address this challenge when interfaces are rough
Solution: A fully numerical tool such as the Finite Element Method

## Slide 33: How do rough surfaces scatter?
Surfaces are treated as random processes characterized by:
Roughness
Correlation length
Correlation type

## Slide 34: Impact of Soil Roughness
Rough soil (FEM)
Rough soil (SPM) (semi-analytic)
Rougher soil (FEM)
40o TE incident field
15% soil moisture (silt loam soil).
θ
inc
scat
λ=24 cm, Gaussian soil, {rough: kh=0.5, s=20o, rougher: kh=0.1, s=5o }

## Slide 35: Impact of Soil Moisture
Logarithmic relation between moisture and back-scatter.
Fit parameters depend on soil surface statistics (roughness, correlation length)
λ=24 cm, inc = 40o, Gaussian soil, {kh=0.5, s=20o}.

## Slide 36: Soil moisture : data cube approach
Physics parameters of soil
roughness
Incidence angle
Soil moisture
Data Cube
Radar scattering cross-section: Polarizations
&
Phase
Data cube is pre-computed
A look-up is performed to estimate soil moisture [Current baseline algorithm for SMAP]

## Slide 37: Heterogeneous soil
Soil moisture
Depth
d
Variable
moisture
Constant
moisture
Study the role of:
Wetting or Drying profile
Depth to constant moisture

## Slide 38: Hetero Soil – Radar Return ()
if const 45%
if const 25%
if const 5%
TM (H-pol), λ= 24cm, inc = 40o, { Gaussian rough soil: kh=0.1, s=5o}
Green, purple curves: Drying profiles 5%(top)  25% (bot)
Blue, red curves: Wetting profiles 45%(top)  25% (bot)

## Slide 39: Hetero Soil – Radar Return ()
TM (H-pol), λ= 24cm, inc = 40o, {Gaussian rough soil: kh=0.1, s=5o}
Conclusion
Radar is very sensitive to top λ/2 of soil.
Making assumption of constant soil moisture can lead to large errors, esp. for drying soils
Date cube FAIL!

## Slide 40: How to compute?
Start with Maxwell’s equations
Recall
Combine it into a single equation

## Slide 41: How to compute: FEM
Solve
in each

## Slide 42: FEM : Basis Elements
In each element, field is expanded along Whitney basis
U1
U2
U3
3 unknowns per element
Finite Element Analysis of Antennas and Arrays, J-Ming Jin and DJ. Riley, Wiley 2009
Each basis element has:
Constant tangential component along one edge.
Only normal component along other edges.
(Constant curl)

## Slide 43: FEM : Galerkin Method
Take the wave equation:
Enforce it in a weak sense:
Testing function:
Chosen to be one of the basis functions.
Unknown field:
Expanded in terms of Whitney basis functions.
By having T cycle through the set of basis functions we get N equations in N variables. Sparse system.

## Slide 44: FEM : Boundary Conditions
Air
Soil
Recast equation to delineate contributions from interior and boundary:
Boundary condition should minimize numerical reflection

## Slide 45: FEM: Implementation
Incident field needs to be tapered:
  Reduce edge diffraction
  Minimize error from boundary conditions
|E|
x
g
Gaussian amplitude with beam waist g.
Satisfies the wave equation to order 1/(k0g cosθ)2
The validity of the Kirchhoff approximation for rough surface scattering using a Gaussian roughness spectrum; E Thorsos, JASA, 1988.

## Slide 46: FEM : Implementation
Each edge length must be < λ/20 (λ in the medium)
Sparse system solved using open-source Matrix MUMPS library ~1,500,000 x 2 unknowns takes < 2 min, < 2 GB RAM on 3 GHz CPU
Many open-source sparse solvers available
  Either direct solvers (small problem size)
  Or iterative solvers (larger problems)

## Slide 47: FEM : Monte Carlo
Challenge is unique to remote-sensing: One computation is not good enough
Statistical properties are desired: Ensemble average over instances
Each instance – Unique mesh 8 min per mesh generation, 1 min to solve
Mesh changes only slightly / instance. Inefficient! => Presents a research opportunity, else methods will not be adopted by the community

## Slide 48: Studying vegetated areas

## Slide 49: Review: SAR Polarimetry
Important to keep the wave picture in mind (ray picture fails as obj. )

## Slide 50: Review: SAR Polarimetry

## Slide 51: Representing scatterers: linear pol
1. Scattering matrix [S], and both polarizations:
2. Received voltage in terms of polarizations of Tx,Rx antennas:

## Slide 52: Multi-look averaging
5. Rx/Tx antenna polarizations remain same, [C] is averaged:
4. Simplifies to:
Covariance matrix
3. Gives Rx power as:

## Slide 53: Examples: Dihedral corner reflector and vertical cylinder
Scattering matrix
Covariance matrix

## Slide 54: Cylinders (imp for vegetation)
Rotate by about vertical
So far we had a single [C]. Now let’s ensemble average: <[C]>
Say that is not known, but a uniform random variable [0,

## Slide 55: Scattering from the ground (simpler model than FEM)
Small perturbation method (SPM, 1951 by S. Rice)
Solve Maxwell’s equations with a bare rough interface between air-soil
Assuming low roughness, the equations can be approximated in closed-form
        Gives avg. radar backscatter in terms of soil , incidence angle , mean roughness , and surface correlation length, , and

## Slide 56: Scattering from the ground (simpler model than FEM)

## Slide 57: Something to ponder ..
Observation: All the scattering examples considered so far contain physical details of the scatterers. Example: dihedral/cylinder dimensions, soil roughness
The promise of remote sensing is to infer interesting quantities from space without ground visits
So how can this be accomplished?

## Slide 58: Decomposition models for SAR data
There are many sophisticated models that attempt to solve this problem
We will discuss the simplest of them, by building on the already discussed models
The approach is based on: Freeman, Anthony, and Stephen L. Durden. "A three-component scattering model for polarimetric SAR data." IEEE Transactions on Geoscience and Remote Sensing 36.3 (1998)

## Slide 59: Three-component scattering…
Radar return is theorized to be an incoherent sum of:

## Slide 60: Cylinders – 1
Assuming uniformly random cylinders, we find the components of the averaged covariance matrix
Doing this carefully, we get:

## Slide 61: Double Bounce – 2
Earlier we had:
Now generalize to: Allow ground & trunk to have diff. refl. coefficients and attenuation through canopy

## Slide 62: Ground backscatter – 3
Use the SPM model (also called 1st order Bragg). Recall:
Gives us covariance matrix components as:
IMP: We don’t assume any of the surface properties are known

## Slide 63: Add it all up …
This is the net, normalized power seen by the radar in each channel
4 Eqns in 5 unknowns

## Slide 64: Add it all up …
Certain heuristic assumptions can be used to fix the value of in order to get 4 eqns/4 unknowns
Example of using this model over a test site in Germany using L-band SAR
Good for distinguishing vegetation cover types, also flooding in fields
Moreira, Alberto, et al. "A tutorial on synthetic aperture radar." IEEE Geoscience and remote sensing magazine 1.1 (2013): 6-43.

## Slide 65: Extending it…
A new “helix” scattering term also helps distinguish urban areas from natural areas

## Slide 66: Earth deformation studies

## Slide 67: Oil spill detection & mapping
Moreira, Alberto, et al. "A tutorial on synthetic aperture radar." IEEE Geoscience and remote sensing magazine 1.1 (2013): 6-43.

## Slide 68: Buried pyramid detection
Quickbird has 60 cm radar plus optical/IR frequency sensors.

## Slide 69: SAR interferometry
Recap: Maxwell’s equations lead to the wave equation , which gives harmonic solutions of the form
In SAR interferometry,
  Use 2 radars instead of 1,
  Phase difference between the fields measured by both radars depends on the relative path difference
Even though both radars are 100s of Km, path difference on the order of can be measured

## Slide 70: Interferometry Geometry
Individual phases are:
Usually, , Cosine Law gives:

## Slide 71: Phase plot for flat Earth

## Slide 72: Effect of wavelength

## Slide 73: Example: Mt. Shasta
3D digital elevation model below:

## Slide 74: Interferogram for Mt Shasta

## Slide 75: Remove “flat” Earth
be a point on flat Earth
Earlier term: gets re-written as:
Simplify interferometric phase:
First term is constant: “Flat” Earth

## Slide 76: “Flattened” interferogram

## Slide 77: Sensitivity to topography
Objective is to find the height of the surface,
Simple geometry gives:
And
Ambiguity if exceeds

## Slide 78: Sensitivity to topography
Smaller ambiguity height => Better resolution, but the phase will get “wrapped” around
Active research area: phase unwrapping algorithms

## Slide 79: Phase wrapping depends on

## Slide 80: Example of phase unwrapping: DEM
(a) With flat Earth, (b) after removal of flat earth (c) after phase unwrapping
Taken by TanDEM-X over Atacama desert in Chile

## Slide 81: Two ways to implement InSAR

## Slide 82: Single v/s Repeat pass InSAR
Single pass
Baseline known
Large baselines not possible
No temporal decorrelation
Higher cost and better performance
NISAR will do this!
Repeat pass
Baseline not well known/changing
Large baselines possible
High temporal decorrelation
Low cost

## Slide 83
In summary, the possibilities are endless!

## Slide 84: Further reading …
Most figures taken from these references with due credit to them, and to Jakob van Zyl